## Slide 1: Gesture recognition using smart watch
Steven Wang
--progress report

## Slide 2: Project introduction
Allow a driver wearing a smart watch to use wrist and hand gestures to navigate through a watch app while keeping the watch bearing hand on the steering wheel.
Single / double outside rotation
Single / double inside rotation
Grip gesture

## Slide 3: Current status
Current status:
  Free hand gesture classification
    Single outside
    Single inside
    Double outside
    Double inside
    Grip
  Simple implementation using SDL

## Slide 4: System flow chart
Raw data collection
Data processing
Extract statistic features
Build classifier
Correlation analysis
Data processing
Extract required features
Error analysis
Training
Testing

## Slide 5: Data collection
x
y
z
Linear Accelerometer
  The linear acceleration sensor provides a three dimensional vector representing acceleration along each device axis, excluding gravity
Gyroscope
  The gyroscope measures the rate of rotation in rad/s (angular speed) around a device’s x, y, and z axis.

## Slide 6: Data visualization – double inside
sqrt(acc_x2 + acc_y 2 + acc_z2)
Sqrt(gro_x2 + gro_y 2 + gro_z2)
acc magnitude
gro magnitude

## Slide 7: Relative angular speed
Define:
  Set the angular speed magnitude at the first point as the speed reference value, label as as0
  Label the relative angular speed at nth point as rAsn. Label the angular speed magnitude at nth point as asn
  rAsn = asn – as0
Formula:
  aslast = ascurrent
  ascurrent= sqrt(gro_x2 + gro_y 2 + gro_z2)
  delta = ascurrent- aslast
  rAsn = rAsn-1 * 0.9 + delta
Double inside gro_magnitude
Double inside rAs

## Slide 8: Plot of relative angle speed
single inside
double outside
double inside
single outside

## Slide 9: Event trigger and feature extraction
Data chunk period
Trigger threshold
Time sync with rAs
Algorithm:
  rAsarr=[] accYarr=[] timer initial
  trigger = false
  if rAs>triggerThreshold and !trigger: trigger = true
  timer start for 1 data chunk period:
  rAsarr.append(rAs) accYarr.append(accY) timer reset
  trigger = false
Relative angular speed
acc_y

## Slide 10: Feature extraction
single outside
single inside
double inside
double outside
single outside
single inside
double outside
Double inside
peakarr=[]
for i in range1,len(rAsarr): if rAsarr[i]>rAsarr[i-1] and rAsarr[i]>rAsarr[i+1]: peakarr.append(rAsarr[i])
Feature 1: # of peakarr = len(peakarr)
Feature 2: min_accY = min(accYarr)
rAsarr
accYarr

## Slide 11: Classification
Decision tree
  Value = [so,si,do,di]
# of peakarr>=peakThresh
min_accY<accY thresh
Value = [0,0,1,1]
min_accY<accY thresh
Value = [1,1,0,0]
True
False
Value = [0,0,0,1]
Value = [0,0,1,0]
Value = [0,1,0,0]
Value = [1,0,0,0]
True
False
False
True

## Slide 12: Validation
Single Outside | Single Inside | Double Outside | Double Inside
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
so | si | do | di
100% | 100% | 100% | 100%
Single Outside | Single Inside | Double Outside | Double Inside
SO | SI | SO | DI
SO | SI | SO | SI
SO | SI | DO | DI
SO | SI | SO | DI
SO | SI | SO | SI
SO | SI | SO | DI
SO | SI | SO | DI
SO | SI | SO | DI
SO | SI | DO | DI
SO | SI | SO | DI
SO | SI | SO | DI
100% | 100% | 20% | 80%
free hand
Holding steering wheel
Trigger threshold = 10
Data period = 1s
peakThresh = 2
accY thresh = -15

## Slide 13: Validation
Single Outside | Single Inside | Double Outside | Double Inside
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DI | DI
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DO | DI
SO | SI | DO | DI
100% | 100% | 90% | 100%
Single Outside | Single Inside | Double Outside | Double Inside | Single Inside
SO | SI | DO | DI | SI
SO | SO | DO | DI | SI
SO | SI | DO | DI | SI
SO | SI | DI | DI | SI
SO | SI | DO | DI | SO
SO | SO | DO | DI | SI
SO | SO | DO | DI | SI
SO | SI | DO | DI | SI
SO | SI | DO | DI | SI
SO | SI | DO | DI | SI
SO | SI | DO | DI | SI
100% | 70% | 90% | 100% | 90%
free hand
Holding steering wheel
Trigger threshold = 6
Data period = 1s
peakThresh = 2
accY thresh = -15

## Slide 14: Grip gesture
Issues:
  Watch tightness and position variability has a significant effect on the sensor results
  High order integrate of sensor value decrease the sensor accuracy dramatically.

## Slide 15: Demo 1

## Slide 16: Demo 2