## Slide 1: Gesture recognize 09-12-2016
Steven Wang

## Slide 2: Previous question
The X axis is horizontal and points to the right
The Y axis is vertical and points up
The Z axis points towards the outside of the front face of the screen.
In this system, coordinates behind the screen have negative Z values.

## Slide 3: Project plan
Phase 1: Offline model
  Collect the gesture data in 2 seconds period
  Find out the meaningful features
  Find out the good performance classifiers
Phase 2: Real time model
  Define the gesture event trigger time
  Implement the features and classifier from phase 1 into android app.

## Slide 4: Data collection
Send record signal
Start Acc & Gyo sensor and record ACC(x, y, z) and GYO(x, y,z) for 2 seconds
Send the 2 seconds ACC and GYO data list back to the phone
Send the 2 seconds ACC and GYO data list to the laptop
Reformat and remove the dirty data
and save ACC and GYO
file separately

## Slide 5: Rise the sample frequency
ACC_X
ACC_Y
ACC_Z
GYO_X
GYO_Y
GYO_Z

## Slide 6: Data process
Step 1: read from one of the 8 files (single_inside_acc, single_inside_gry, single_outside_acc, single_outside_gry, double_inside_acc, double_inside_gry, double_outside_acc, double_outside_gry)
Step 2: for each line of the input stream, remove the none numerical character and uncompleted data (the data not in 3 dimension)
Step 3: synchronize the _acc and _gry files with the time stamp.
Step 4: concatenate the all the single inside, single outside, double inside and double outside files data.

## Slide 7: Feature extraction and target labeling
Features:
  △t: the time difference between the sensor value change
  Statistic features: max, min, mean, std within a window size (20 points).
  e.g.
  There are 4 statistic features for each direction. The total feature dimension is: 4*3*2+1 = 25
Target labeling:
  Single outside: 1
  Single inside: 2
  Double outside: 3
  Double inside: 4

## Slide 8: Data visualization
…

## Slide 9: Machine learning model -- SVM
Given a set of training examples, each marked for belonging to several categories, an SVM training algorithm builds a model that assigns new examples into correct category. An SVM model is a representation of the examples as points in space, mapped so that the examples of the separate categories are divided by a clear gap that is as wide as possible.
Predict result
Label
accuracy

## Slide 10: Train and test
After the data processing, 80 percentage of data is randomly selected as training data. The rest 20 percentage of data is for testing.
10 fold cross validation: average confidence is 97.10%
However, in the test demo program, the saved model performance is not very accurate.

## Slide 11: Next step
Why the cross validation result is good but the test demo cannot perform well?
  Recollect more sets (20~25) of training data for each guesture.
  Make each class has the same sample data
Extract other meaning features:
  Yaw, pich angle
Use a physical model instead of using machine learning